## Slide 1: VORTEX
DESIGN OF
HANDY WASHING MACHINE

## Slide 2: INTRODUCTION
A novel washing machine that is cheap, portable, compact and easy to use.

## Slide 3: THE CONCEPT OF WASHING
Soap has ions that have both hydrophilic and hydrophobic ends that are used in making dirt ions (that are hydrophobic) mobile.
A washing machine simply induces agitation.

## Slide 4: FEATURES
-Light weight/Portable
-Timer
-Level detector
-Noiseless operation
-No vibration
-Stable
-Tangle free operation

## Slide 5: PUMPS AND STRUCTURE
Three pumps are fitted in an optimized configuration to create a clockwise vortex. These are noiseless, compact, submersible pumps that have a pump head of 1.2m.

## Slide 6: TIMER
An ATMega16A-PU
40-Pin Microcontroller is being used
To implement a 5-minute and
A 10-minute timer.

## Slide 7: ALGORITHM FLOWCHART

## Slide 8
Start
If
TimerB=1 AND Level sensor=1
Machine works till
10 min
Machine works till
5 min
If
TimerA=1 AND Level sensor=1
yes
yes
no
no

## Slide 9: CODING ATMEGA 16

## Slide 10
#include<avr/io.h>
assign portA.1=timer_5;
assign portA.2=timer_10;
assign portA.3=level_sensor;
assign portB.1=relay_op;
void main()
{
DDRA portA=#FFxh; // port a is set as input from timer switch
DDRA portB=#00xh;
while(1)
{
if(timer_5==1 && level_sensor==1) %delay generation
{
for(int i=0;i<=500;i=i+1)
{
relay_op=#01xh;
for(int j=0;j<=10000;j=j+1);
}
relay_op=#00xh;
break; % as soon as 5 minutes is over it comes out of loop
}
if(timer_10==1 && level_sensor==1)
{
for(int i=0;i<=500;i=i+1)
{
relay_op=#01xh;
for(int j=0;j<=10000;j=j+1);
}
relay_op=#00xh;
break;
}
}
}

## Slide 11: LEVEL DETECTON
A pair of probes are attached to the top of the instrument, at the appropriate depth, which shall detect continuous water
Between the two.

## Slide 12: COST ESTIMATION
PER UNIT (OFF THE SHELF)
Submersible Pump – 1200/-
ATMEGA16 Controller – 270/-
Relay – 75/-
Misc. Electronics – 300/-
Misc. Frame – 150/-
NET – 1995/-

## Slide 13: COST ESTIMATION
PER UNIT
(LARGE SCALE PRODUCTION)
Submersible Pump – 600/-
ATMEGA16 Controller – 100/-
Relay – 50/-
Misc. Electronics – 100/-
Misc. Frame – 100/-
NET – 950/-

## Slide 14
THANK YOU